## Slide 1: Therapeutic Physical Modalities
Angie Guggino, MS, ATC, LAT

## Slide 2: Learning Target
The use and effectiveness of physical modalities.

## Slide 3: Therapeutic Modalities
Heating, cooling, and mechanical/electrical methods of treatment used on the human body
Hot and cold treatments, therapeutic ultrasound, and various electrical modalities

## Slide 4: Therapeutic Modalities
Used along with other forms of treatment
  To relieve pain, reduce or retard swelling, decrease spasm, and promote healing
Can minimize time lost from participation
Used improperly, condition may worsen

## Slide 5: Cryotherapy
Use of cooling agents (e.g., cold packs, cold bucket baths, and ice massage)
Most widely used therapy
Responses include
  reduction of tissue metabolism
  decreased nerve conduction velocity
  reduced muscle spasm
  secondary vasodilatation
  increase in muscle strength after treatment
If left on too long, counter effects may occur

## Slide 6: Ice packs
Effective for local areas of concern
Quick and economical
  Plastic bags with ice cubes
  Gel packs
  Chemical-activated cold pack

## Slide 7: Ice Packs

## Slide 8: Cryotherapy
Ice massage
  Used for localized problems (e.g., tennis elbow)
  Only takes about five – ten minutes
Cold water compression
  Cold and compression applied simultaneously
  Cryo-cuff
Ice baths
  Immersion in a bucket of ice water or whirlpool
  Allows complete, uniform coverage
  Some exercise movements may be performed

## Slide 9: Ice Massage

## Slide 10: Contraindications and Precautions
Cryotherapy should be used with caution on persons who have:
  Thermoregulatory problems
  Sensory deficits
  Hypersensitivity to cold
  Impaired circulation
  Heart disease
  Malignant tissue

## Slide 11: Heating Agents
Heat is applied superficially (skin deep), or with a modality capable of heating tissues up to a few inches beneath the skin
Beneficial effects:
  Reduced pain
  Promotion of healing
  Increased range of motion
  Muscle relaxation

## Slide 12: Heating Agents
Localized vigorous heating effects:
  Substantially increased vasodilatation
  Increased metabolic rate and capillary pressure and flow
  Clearance of metabolites
  Oxygenation of tissue

## Slide 13: Hydrocollator Packs
Moist hot packs used for superficial heating
Kept warm in a heated stainless-steel container filled with hot water in the range of 160o F
Left in place for 10 to 20 minutes

## Slide 14: Hydrocollator Packs

## Slide 15: Contraindications and Precautions
Heat is not used until 48 to 72 hours after injury
  Heat dilates the vessels and could cause additional bleeding if healing is not adequate
Heat should not be used:
  Acute injury
  Athletes with impaired circulation
  Areas of diminished sensation
  Athletes who may be heat intolerant

## Slide 16: Hydrotherapy
Superficial heating
Agitated, heated water in a whirlpool
Larger area on an extremity can be treated
Athlete can perform range-of-motion exercises while in whirlpool

## Slide 17: Contrast Therapy
Alternating hot and cold water bath for specified time periods
May be used in the sub-acute injury stage
  48 to 72 hours after the injury occurs

## Slide 18: Ultrasound
Deep-heating modality
Not recommended during acute injury stage

## Slide 19: Diathermy
high-frequency electric current is delivered via shortwave, microwave, or ultrasound to generate deep heat in body tissues

## Slide 20: Paraffin bath
Wax

## Slide 21: Electrical Modalities
Pass electrical currents through skin into the body causing nerve tissue stimulation
Use is limited by law
Two main categories:
  Electrical stimulation
  Transcutaneous electrical nerve stimulation

## Slide 22: Electrical Stimulation
E-stim or muscle stim
Effects include:
  increasing range of motion and muscle strength
  reeducating muscles
  improving muscle tone
  controlling pain
Neuromuscular electrical stimulation is most common

## Slide 23: Transcutaneous Electrical Nerve Stimulation
T.E.N.S.
Commonly applied with a portable unit for pain control
Electric current is applied through a surface electrode pad that is in contact with the external skin surface

## Slide 24: E-stim

## Slide 25: Contraindications
Electrical stimulation should not be used:
  Over the carotid sinus
  During pregnancy
  In individuals with pacemakers
  On people who are sensitive to electricity
  Any time active motion is contraindicated

## Slide 26: Manual Modalities
Massage
Intermittent compression unit
Traction

## Slide 27: Medications
Anti-pyretic
Anti-inflammatory
Analgesic
Anti-fungal
Gastrointestinal
Antibiotics
Asthma medication

## Slide 28: Rx vs. OTC’s
Prescription medications require physician approval
Over-the-counter medications are often less doses of prescription medications

## Slide 29: Anti-Pyretic
Used to decrease fever
Acetaminophen (Tylenol)
Ibuprofen (Motrin, Advil)
Aspirin

## Slide 30: Anti-inflammatory
Steroidal requires Rx
  prednisone
Non-Steroidal (NSAIDS) – Rx
  diclofenac (Cambia, Cataflam, Voltaren)
  etodolac (Lodine)
  fenoprofen (Nalfon)
  flurbiprofen (Ansaid)
  naproxen (Anaprox, Naprosyn)
  oxaprozin (Daypro)
Non-steroidal (NSAIDS) - OTC
  Ibuprofen (Motrin, Advil)
  Aspirin
  Naproxen (Aleve)

## Slide 31: Analgesic
Pain killers
Rx usually narcotic
  Morphine, hydrocodone, fentanyl oxycodone
OTC’s
  Aspirin, Tylenol, NSAID’s

## Slide 32: Asthma Medication
Long-term control to prevent attacks
  Rx only
Quick-relief from attack symptoms
  Rx only
  Albuterol
OTC medication provide temporary relief
  Primatene Mist and Bronkaid

## Slide 33: Common in Sports Medicine
Anti-fungal: used to treat a variety of fungal infections
  Ring worm, jock itch, athlete’s foot
Gastrointestinal: used to treat a variety of conditions
  Nausea, diarrhea, gas, acid reflux
Antibiotics: used to treat bacterial infections
  Topical and oral
  Several different classifications

## Slide 34: The End